## Slide 1: The Memory Hierarchy Introduction to Computer Systems 12th Lecture

## Slide 2: 来点CSAPP笑话
Q：为什么CSAPP把最困难的内容放到课程开始，而把简单的内容放到后面？
A：因为作者们深刻理解了浮点数的舍入误差，这样可以最小化课程的总难度。

## Slide 3
DDR5 memory access latency: avg. 70 ns
Modern CPU clock length: 0.3ns
How can the access to DRAM be done
in one cycle?

## Slide 4: Today
Program exhibits locality
Cache exploits locality (more in the next lecture)
Faster storage devices stores less data and are more expensive, and vice versa.

## Slide 5: Locality
The locality Principle: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 6: Locality Example
Data references
  Reference array elements in succession: accessing a[i] means e.g., a[i-1], and a[i+1] are likely to be referenced
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Temporal locality
Spatial locality
Temporal locality

## Slide 7: Qualitative Estimates of Locality
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Question: Does this function have good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}

## Slide 8: Locality Example
Question: Does this function have good locality with respect to array a?
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
Answer: no, unless…
M is very small

## Slide 9: Locality Example
Question: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum;
}
Answer: make j the inner loop

## Slide 10: How to write a program with poor locality in instruction accesses?

## Slide 11: Is locality only applicable to program? Can we have some other examples of locality?

## Slide 12: System design principles: how to optimize
Optimizing a system layer requires exploiting the properties of the layer above it and the layer below it.
Suppose that we would like to optimize an OS
The layer above it: program, which often exhibits locality
The layer below it: hardware, which is amenable to pipelining.

## Slide 13: Today
Program exhibits locality
Cache exploits locality (more in the next lecture)
Faster storage devices stores less data and are more expensive, and vice versa.

## Slide 14: Caches
Cache: A smaller, faster storage device that stores frequently accessed data in a larger, slower device.
Why does caching work?
  Because of locality, programs often access a subset of key data given a time interval.
  Cache can just store this subset of key data.
Big Idea (Ideal): Most data stores in the cheap, slow storage, but that access at the rate of the fast storage.

## Slide 15: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Underlying
device
4
4
4
10
10
10
The underlying devices are divided into multiple blocks.

## Slide 16: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!
How does this exploit locality?

## Slide 17: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes (more next lecture)
Replacement policy: determines which block gets evicted (victim)

## Slide 18: General Caching Concepts: Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache is empty.
Conflict miss (more next lecture)
    Due to block mapping between the caching and the underlying device.
    E.g. Cache block N, stores the block % 4, referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.
What to do with different kinds of misses in the system?

## Slide 19: Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
L2 cache
(SRAM)
Each layer caches the data of the next layer!
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L6:
The two memory modules in the processor figure actually refer to the L1 cache.

## Slide 20: Examples of Caching in the Mem. Hierarchy
Hardware MMU
0  > <1
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB pages
64-byte blocks
64-byte blocks
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
4
On-Chip L1
Hardware
10
On-Chip L2
NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0  <1
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 21: Examples of Caching in the Mem. Hierarchy
Web cache
Network file systems cache
Memory
L2 cache
L1 cache
Registers
Cache Type
Web proxy server
300,000,000
Remote serves
Hardware
4
CPU core
Hardware
15
CPU core
NFS client
15,000,000
Local disk
OS
100
Main memory
Compiler
1
CPU core
Managed By
Latency (cycles)
Where is it?
Disk cache
Disk controller
150,000
Disk firmware
L3 cache
Hardware
50
CPU core

## Slide 22: 来点CSAPP笑话
学生：老师，我发现 CSAPP 课件里有错误。
老师：很好！学习计算机系统就是要有质疑精神。
学生：所以这道考试题的答案是不是也应该修改？
老师：学习计算机系统的另一个重要原则，是尊重接口规范。

## Slide 23: Why the main memory is slow? Reason #1: the medium

## Slide 24: RAM Technologies
DRAM
Implementing the main memory
Must refresh state periodically
SRAM
Implementing cache
Holds state indefinitely (as long as power-on)

## Slide 25: SRAM vs DRAM Summary
Both SRAM and DRAM reach their limits with semiconductor technology
  DRAM scaling limited by need for minimum capacitance
    Aspect ratio limits how deep can make capacitor
    DRAM cell cannot be made smaller, because then it stops to store data reliably
Trans. Access Needs Needs
per bit time refresh? ECC? Cost Applications
SRAM 6 or 8 1x No Yes 100x Cache
DRAM 1 10x Yes Yes 1x Main memories,
frame buffers
ECC: Error correction code

## Slide 26: Enhanced DRAMs
Basic DRAM cell has not changed since its invention in 1966.
  Commercialized by Intel in 1970.
DRAM cores with better interface logic and faster I/O :
  Synchronous DRAM (SDRAM)
    Sends one bit per cycle (rising or falling)
    Uses a conventional clock signal instead of asynchronous control
    Allows reuse of the row addresses (e.g., RAS, CAS, CAS, CAS)
  Double data-rate synchronous DRAM (DDR SDRAM)
    Sends two bits per cycle (rising and falling)
    Different types distinguished by size of small prefetch buffer:
      DDR (2 bits), DDR2 (4 bits), DDR3 (8 bits), DDR4 (16 bits)
    By 2010, standard for most server and desktop systems
    Intel Core i7 supports DDR3 and DDR4 SDRAM

## Slide 27: Conventional DRAM Organization
d x w DRAM:
  dw total bits organized as d supercells of size w bits
cols
rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
addr
data
supercell
(2,1)
2 bits
/
8 bits
/
Memory
controller
(to/from CPU)

## Slide 28: Reading DRAM Supercell (2,1)
Step 1(a): Row access strobe (RAS) selects row 2.
Step 1(b): Row 2 copied from DRAM array to row buffer.
Cols
Rows
RAS = 2
0
1
2
3
0
1
2
Internal row buffer
16 x 8 DRAM chip
3
addr
data
2
/
8
/
Memory
controller

## Slide 29: Reading DRAM Supercell (2,1)
Step 2(a): Column access strobe (CAS) selects column 1.
Step 2(b): Supercell (2,1) copied from buffer to data lines, and eventually back to the CPU.
Cols
Rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
CAS = 1
addr
data
2
/
8
/
Memory
controller
supercell
(2,1)
supercell
(2,1)
To CPU

## Slide 30: Memory Modules
: supercell (i,j)
64 MB
memory module
consisting of
eight 8Mx8 DRAMs
addr (row = i, col = j)
Memory
controller
DRAM 7
DRAM 0
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit word main memory address A
bits
0-7
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63
64-bit word
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56

## Slide 31: Why the main memory is slow? Reason #2: the bus

## Slide 32: Traditional Bus Structure Connecting CPU and Memory
A bus is a collection of parallel wires that carry address, data, and control signals.
Buses are typically shared by multiple devices.
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus

## Slide 33: Memory Read Transaction (1)
CPU places address A on the memory bus.
ALU
Register file
Bus interface
A
0
A
x
Main memory
I/O bridge
%rax
Load operation: movq A, %rax

## Slide 34: Memory Read Transaction (2)
Main memory reads A from the memory bus, retrieves word x, and places it on the bus.
ALU
Register file
Bus interface
x
0
A
x
Main memory
%rax
I/O bridge
Load operation: movq A, %rax

## Slide 35: Memory Read Transaction (3)
CPU read word x from the bus and copies it into register %rax.
x
ALU
Register file
Bus interface
x
Main memory
0
A
%rax
I/O bridge
Load operation: movq A, %rax

## Slide 36: Memory Write Transaction (1)
CPU places address A on bus. Main memory reads it and waits for the corresponding data word to arrive.
y
ALU
Register file
Bus interface
A
Main memory
0
A
%rax
I/O bridge
Store operation: movq %rax, A

## Slide 37: Memory Write Transaction (2)
CPU places data word y on the bus.
y
ALU
Register file
Bus interface
y
Main memory
0
A
%rax
I/O bridge
Store operation: movq %rax, A

## Slide 38: Memory Write Transaction (3)
Main memory reads data word y from the bus and stores it at address A.
y
ALU
Register file
Bus interface
y
main memory
0
A
%rax
I/O bridge
Store operation: movq %rax, A

## Slide 39: Why disks are slow?

## Slide 40: Storage Technologies
HDD: hard disk drive
Store on magnetic medium
SSD: solid state drive
Non-volatile (Flash) Memory

## Slide 41
Comments: SSD actually dominates

## Slide 42
Comments: SSD actually dominates

## Slide 43: 来点CSAPP笑话
学生：“老师，都 2026 年了，为什么 CSAPP 课件中的数据还停留在 2015 年？”
老师：“这是为了让你们更好地理解局部性。”
学生：“什么局部性？”
老师：“时间局部性。CSAPP 的作者认为，2015 年的数据将来还会经常被访问。”

## Slide 44: Why disks are slow? Reason #1: the medium itself

## Slide 45: What’s Inside A Disk Drive?
Spindle
Arm
Actuator
Platters
Electronics
(including a
processor
and memory!)
SCSI
connector
Image courtesy of Seagate Technology

## Slide 46: Disk Geometry (Muliple-Platter View)
Disks consist of platters, each with two surfaces.
Surface 0
Surface 1
Surface 2
Surface 3
Surface 4
Surface 5
Spindle
Platter 0
Platter 1
Platter 2
Notes: Cylinder： 柱面

## Slide 47: Disk Geometry
Each surface consists of concentric rings called tracks.
Spindle
Surface
Tracks
Track k
Sectors
Notes: Sector 扇区

## Slide 48: Disk Operation (Single-Platter View)
The disk surface
spins at a fixed
rotational rate
seek: by moving radially, the arm can position the read/write head over any track.
The read/write head
is attached to the end
of the arm and flies over
the disk surface on
a thin cushion of air.
spindle
spindle
spindle
spindle
spindle

## Slide 49: Disk Operation (Multi-Platter View)
Arm
Read/write heads
move in unison
from cylinder to cylinder
Spindle

## Slide 50: Disk Access
Head in position above a track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 51: Disk Access
Rotation is counter-clockwise
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 52: Disk Access – Read
About to read blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 53: Disk Access – Read
After BLUE read
After reading blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 54: Disk Access – Read
After BLUE read
Red request scheduled next
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 55: Disk Access – Seek
After BLUE read
Seek for RED
Seek to red’s track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 56: Disk Access – Rotational Latency
After BLUE read
Seek for RED
Rotational latency
Wait for red sector to rotate around
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 57: Disk Access – Read
After BLUE read
Seek for RED
Rotational latency
After RED read
Complete read of red
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 58: Disk Access – Service Time Components
After BLUE read
Seek for RED
Rotational latency
After RED read
Data transfer
Seek
Rotational
latency
Data transfer
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 59: Disk Access Time
Average time to access some target sector approximated by:
  Taccess = Tavg seek + Tavg rotation + Tavg transfer
Seek time (Tavg seek)
  Time to position heads over cylinder containing target sector.
  Typical Tavg seek is 3—9 ms
Rotational latency (Tavg rotation)
  Time waiting for first bit of target sector to pass under the head.
  Typical rotational rate = 7,200 RPMs
  Tavg rotation = 1/2 x 1/RPMs x 60 sec/1 min = 4.17ms.
Transfer time (Tavg transfer)
  Time to read the bits in the target sector.
  Tavg transfer = 1/RPM x 1/(avg # sectors/track) x 60 secs/1 min
time for one rotation (in minutes)
fraction of a rotation to be read

## Slide 60: Disk Access Time Example
Given:
  Rotational rate = 7,200 RPM
  Average seek time = 9 ms
  Avg # sectors/track = 400
Derived:
  Tavg rotation = 1/2 x (60 secs/7200 RPM) x 1000 ms/sec = 4.17 ms
  Tavg transfer = 60/7200 x 1/400 x 1000 ms/sec = 0.02 ms
  Taccess = 9 ms + 4.17 ms + 0.02 ms
Important points:
  Access time dominated by seek time and rotational latency.
  First bit in a sector is the most expensive, the rest are free.
  SRAM access time is about 4 ns/doubleword, DRAM about 60 ns
    Disk is about 40,000 times slower than SRAM,
    2,500 times slower than DRAM.

## Slide 61: Why disks are slow? Reason #2: the I/O bus

## Slide 62: I/O Bus
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Expansion slots for
other devices such
as network adapters.

## Slide 63: Reading a Disk Sector (1)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
mouse
keyboard
Monitor
Disk
I/O bus
Bus interface
CPU initiates a disk read by writing a command, logical block number, and destination memory address to a port (address) associated with disk controller.

## Slide 64: Reading a Disk Sector (2)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
Disk controller reads the sector and performs a direct memory access (DMA) transfer into main memory.

## Slide 65: Reading a Disk Sector (3)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
When the DMA transfer completes, the disk controller notifies the CPU with an interrupt (i.e., asserts a special “interrupt” pin on the CPU)

## Slide 66: 来点CSAPP笑话
学生：“CSAPP 的作者一定深刻掌握了空间局部性。”
老师：“为什么？”
学生：“他们解释一个概念的时候，总是假设我已经理解了其它相关的十个概念。”

## Slide 67: Disk Capacity
Capacity: maximum number of bits that can be stored.
  Often in gigabytes (GB), where 1 GB = 109 Bytes.
Capacity is determined by these technology factors:
  Recording density (bits/in): number of bits that can be squeezed into a 1 inch segment of a track.
  Track density (tracks/in): number of tracks that can be squeezed into a 1 inch radial segment.
  Areal density (bits/in2): product of
  recording and track density.
Tracks

## Slide 68: Recording zones
Modern disks partition tracks into disjoint subsets called recording zones
  Each track in a zone has the same number of sectors, determined by the circumference of innermost track.
  Each zone has a different number of sectors/track, outer zones have more sectors/track than inner zones.
  So we use average number of sectors/track when computing capacity.
Spindle
…

## Slide 69: Computing Disk Capacity
Capacity = (# bytes/sector) x (avg. # sectors/track) x
(# tracks/surface) x (# surfaces/platter) x
(# platters/disk)
Example:
  512 bytes/sector
  300 sectors/track (on average)
  20,000 tracks/surface
  2 surfaces/platter
  5 platters/disk
Capacity = 512 x 300 x 20000 x 2 x 5
= 30,720,000,000
= 30.72 GB

## Slide 70: Solid State Disks (SSDs)
Pages: 512KB to 4KB, Blocks: 32 to 128 pages
Data read in units of pages.
Data written only after its block has been erased
Flash
translation layer
I/O bus
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
Flash memory
Solid State Disk (SSD)
Requests to read and
write logical disk blocks

## Slide 71: SSD Performance Characteristics
Benchmark of Samsung 940 EVO Plus
Benchmark of Micron 9650
Sequential access faster than random access
Random writes are somewhat slower
  Erasing a block takes a long time (~1 ms).
  Modifying a block page requires all other pages to be copied to new block.
  Optimization: flash translation layer allows accumulating series of small writes before doing block write.
Sequential read throughput 2,126 MB/s Sequential write tput 1,880 MB/s
Random read throughput 140 MB/s Random write tput 59 MB/s
https://ssd.userbenchmark.com/SpeedTest/711305/Samsung-SSD-970-EVO-Plus-250GB
Sequential read throughput 2,8000 MB/s Sequential write tput 14000 MB/s
Random read throughput 2,2500 MB/s Random write tput 3690 MB/s

## Slide 72: SSD Tradeoffs vs Rotating Disks
Advantages
  No moving parts  No seeking, and rotational overhead, less power
Disadvantages
  Have the potential to wear out
    Mitigated by “wear leveling logic” in flash translation layer
  In 2019, about 4 times more expensive per byte
    And, relative cost will keep dropping
Applications
  In 2019, MP3 players, smart phones, laptops
  In 2026, dominates in desktops and servers

## Slide 73: Comments: the SSD wear out
Not as bad as you thought
  Only affects write, not read
  Even for write: Samsung 990 PRO SSD: 600 TBW (terabytes written).
  That's equivalent to writing 100 GB per day for about 16 years.
An HDD is likely to fall after 16 years as well: the mechanical parts can wear out

## Slide 74: The CPU-Memory Gap, i.e., the memory wall
The gap widens between DRAM, disk, and CPU speeds.
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
DRAM
CPU
SSD
Disk

## Slide 75: Nonvolatile Memories
DRAM and SRAM are volatile memories
  Lose information if powered off.
Nonvolatile memories retain value even if powered off
  Read-only memory (ROM): programmed during production
  Programmable ROM (PROM): can be programmed once
  Eraseable PROM (EPROM): can be bulk erased (UV, X-Ray)
  Electrically eraseable PROM (EEPROM): electronic erase capability
  Flash memory: EEPROMs. with partial (block-level) erase capability
    Wears out after about 100,000 erasings
  3D XPoint (Intel Optane) & emerging NVMs
    New materials
Uses for Nonvolatile Memories
  Firmware programs stored in a ROM (BIOS, controllers for disks, network cards, graphics accelerators, security subsystems,…)
  Solid state disks (replace rotating disks in thumb drives, smart phones, mp3 players, tablets, laptops,…)
  Disk caches

## Slide 76: 来点CSAPP笑话
一个读者愤怒地问CSAPP的作者 “为什么你们的书又长又难读”？
CSAPP的作者说“这正说明我们深刻地理解了系统底层原理：容量大的设备访问速度自然就慢了！”

## Slide 77: Supplemental slides

## Slide 78: Storage Trends
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/MB 880 100 30 1 0.1 0.06 0.02 44,000
access (ns) 200 100 70 60 50 40 20 10
typical size (MB) 0.256 4 16 64 2,000 8,000 16.000 62,500
DRAM
SRAM
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/GB 100,000 8,000 300 10 5 0.3 0.03 3,333,333
access (ms) 75 28 10 8 5 3 3 25
typical size (GB) 0.01 0.16 1 20 160 1,500 3,000 300,000
Disk
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/MB 2,900 320 256 100 75 60 25 116
access (ns) 150 35 15 3 2 1.5 1.3 115

## Slide 79: CPU Clock Rates
1985 1990 1995 2003 2005 2010 2015 2015:1985
CPU 80286 80386 Pentium P-4 Core 2 Core i7(n) Core i7(h)
Clock
rate (MHz) 6 20 150 3,300 2,000 2,500 3,000 500
Cycle
time (ns) 166 50 6 0.30 0.50 0.4 0.33 500
Cores 1 1 1 1 2 4 4 4
Effective
cycle 166 50 6 0.30 0.25 0.10 0.08 2,075
time (ns)
Inflection point in computer history
when designers hit the “Power Wall”
(n) Nehalem processor
(h) Haswell processor